## Slide 1: Project Seminar On Modeling of Armature Controlled D.C Motor Using MATLAB

## Slide 2: What is DC Motor
A direct current (DC) motor is a fairly simple electric motor that uses electricity and a magnetic field to produce torque, which turns the motor.
A dc motor is used to convert electrical energy into mechanical energy for driving loads.

## Slide 3: PRINCIPLE OF OPERATION
The operation of a dc motor is based on electromagnetism.
A current -carrying conductor generates a magnetic field; when this is then placed in an external magnetic field, it will experience a force proportional to the current in the conductor, and to the strength of the external magnetic field.

## Slide 5: METHODS OF SPEED CONTROL OF DC MOTOR
N=K V-IaRa\ r.p.s Flux\ Pole
Flux control method.
Rheostatic Control method.
Voltage control method.

## Slide 6: Armature controlled method
In the armature voltage control method, the voltage applied to the armature circuit, Va is varied without changing the voltage applied to the field circuit of the motor. Therefore, the motor must be separately excited to use armature voltage control.
When the armature voltage is increased, the no-load speed of the motor increases while the slope of the torque-speed curve remains unchanged since the flux is kept constant [10].